## Slide 1
2019 beach assessment update:
Town of Southern Shores, NC
Ken Willson
Program Manager
Wilmington, North Carolina

## Slide 2: Presentation Outline:
Background
Volume Changes (Updates)
Volume and Cost Updates
Schedule
Recommendations

## Slide 3: Background:
Stated Goals of Beach Management Plan:
  provides a reasonable level of storm damage reduction to public and private development
  mitigates long-term erosion that could threaten public and private development, recreational opportunities, and biological resources
  maintains a healthy beach that supports valuable shorebird and sea turtle nesting habitat
Beach Management Plan recommendations was based on December 2017 survey data
Updated beach profile surveys – May 2019
Beach Management Plan aims to coordinate the efforts of Southern Shores with neighboring communities in Dare County to achieve cost savings where possible

## Slide 4: Background:
Northern
Portion

## Slide 5: Volume Change (Update):
Three (3) Sections Referenced:
  Northern Portion – North Town Boundary to 3rd Ave.
  Main Fill Area – 3rd Ave. to Approx. 400 ft. South of Chicahawk Trl.
  Transition Area - 400 ft. South of Chicahawk Trl. to South Town Boundary
Town Wide – Volume Changes between Dec. 2017 and May 2019
From 3rd Ave. South – Volume Changes between Oct. 2006 and May 2019
From 9th Ave. North – Volume Changes between Sept. 2013 and May 2019

## Slide 6: Volume Change (Update):
Northern Portion:
  Gained sand between Dec. 2017 and May 2019 (5.5 cy/lf./yr.)
  Between Sept. 2013 and May 2019 (5.7 years), northern 2,000 feet of Town (Area north of 9th Ave.) had a volume change rate of +1.3 cy/lf./yr.
Main Fill Area – Gained sand between Dec. 2017 and May 2019 (4.6 cy/lf./yr.)
Transition Area – Lost sand between Dec. 2017 and May 2019 – average of -18.9 cy/lf./yr.)
Area south of 3rd Ave had a long-term average volume change rate of +2.5 cy/lf./yr.
Area south of 3rd Ave had a short-term average volume change rate of -3.0 cy/lf./yr.

## Slide 7: Recommended Beach Fill Options:
Project Extent – Where to Place Sand
Project Volume – How Much Sand To Place
  Historical Volume changes
  Vulnerability Analysis
  Volume Present in the “Volume Envelope”
Notes: Consider Adding a Photo.

## Slide 8: Beach Management Plan: Project Extent (Beach Volumes)

## Slide 9
Option 1: Based on Average Volume Envelope Target of 846 cy/lf. Required 45 cy/ft. Main Fill, 30 cy/ft. Transition Fill – 665,650 cy
Option 2: 30 cy/ft. Main Fill & Transition Fill – 492,300 cy
Option 3: 57 cy/ft. Main Fill, 30 cy/ft. Transition Fill – 803,050 cy
Project extent / project volume:
(Initial Recommendations)

## Slide 10
Project extent / project volume:

## Slide 11
Option 1: Design to 846 cy/lf. and 3 cy/lf erosions rate = 828,400 cy
Option 3: Design to 858 cy/lf. and 3 cy/lf erosion rate = 1,025,800 cy
Updated project volume:

## Slide 12: Storm Damage Reduction Project
Pre-Project Conditions

## Slide 13: Storm Damage Reduction Project
Design
Beach
Design Beach

## Slide 14: Storm Damage Reduction Project
Constructed Beach Fill
Initial Construction

## Slide 15: Storm Damage Reduction Project
Post-Construction
Adjustment in 6-18 months
Equilibration of Beach Fill

## Slide 16: Storm Damage Reduction Project
Advance Fill
Design
Beach
Nourishment Interval

## Slide 17: Storm Damage Reduction Project
Loss of Advance Fill
During Project Interval
Design
Beach
Nourishment Interval

## Slide 18: cost:
Page 22 of the Report

## Slide 19: Schedule:

## Slide 20: Recommendations:
Determine Whether to Pursue Project / Which Option To Pursue
Continue Coordination with County and Neighboring Communities
Initiate Financial Planning
Initiate Permitting and Design of the Beach Fill*
Continued Monitoring of the Beach Profiles (2020)
* Assumes the Town Decides to Pursue a Project

## Slide 21
Ken Willson
  Kenneth.Willson@aptim.com
  910 443 4471
QUESTIONS

## Slide 22
Profile Station 170+56: (8th Ave.)

## Slide 23
Profile Station 170+56: (8th Ave.)

## Slide 24
Area north: (7th Ave)
Photos Taken Sept. 11, 2019: Dry Sand Beach

## Slide 25
Area north: (7th ave)
Photos Taken Sept. 11, 2019: Dune System

## Slide 26
Area north: (7th ave)

## Slide 27: Beach Management Plan: Project Extent (Beach Volumes)

## Slide 28
Beach Management Plan: Project Extent (Beach Volumes)